## Slide 1
Same-Frame Pixel-Level A/B Display
A Zynq-7020 programmable-logic video pipeline that turns the picture itself into an instrument
DATA PATH - entirely in the PL
RGMII
UDP / IP / MAC self-written
DDR ping-pong buffers
zoom 0.25-2x + rotate auto-fit
9-stage effect chain, fixed 15 cycles
A/B seam mixer
OSD + HDMI 1024x600
PS runs a few hundred lines of bare-metal control only; link health is counted in hardware and readable three ways - on screen, over JTAG, over serial.
What is new - each item is falsifiable
1 The display is the measurement
Unprocessed left, processed right, same read address and clock cycle. The seam is fixed, auto-swept, or pinned in image domain so it follows zoom and rotation.
2 Health counted by hardware
Received / dropped / corrupt / CRC / frame-gap statistics with three independent read-outs, and an arbiter whose reported source is the source actually on screen.
3 Bad frames never reach the panel
Triple commit gate - row bitmap, byte budget, no corrupt flag - plus a blanking-window-atomic copy with a watchdog: a torn update is dropped, the old frame is kept.
4 Reproducibility engineered, not claimed
One command runs the gate suite and two full-frame testbenches pinned by md5 to the RTL they check; every criterion must be able to turn red, and every fix has a mutation control.
Measured on the board
+0.553 ns
setup WNS after route,
board build r94
0 / 50883
failing setup endpoints
27.02 %
Slice LUT (FF 7.59 %, BRAM 67.86 %)
33.34 ms
PC-to-screen mean (min/max 20 / 51 ms)
0 of 9000
frames dropped or corrupt in 300 s at 15 MB/s
116.7 fps
unthrottled, still no lost word - no max fps claimed
Also measured: SD playback 29.8-30.0 fps (100-frame window) - frame-interval jitter 22 / 33.33 / 45 ms at 30 fps - DSP48 19 of 220 - dynamic power 2.206 W, estimated junction temperature 52.5 C (tool confidence Low).
Panel 1024x600 at 59.5 Hz, H_TOTAL 1344; source 512x300 RGB565; three sources - GbE, SD card, self-generated test card - arbitrated in the PL.
Honest boundaries: absolute WNS/WHS deltas are neither gain nor loss here - equivalent sources measured a 0.4 ns placement swing between builds. One per-pixel criterion is left deliberately red, documenting an unfixed frame-head wrap-around. Simulation is xsim only, so out-of-array writes are closed out with on-board evidence. r94 is not gate-frozen yet (frozen set: r75).
Vivado / Vitis 2025.2.1 - device xc7z020clg484-2 - sources on GitHub, MIT - every number names the report file it came from (data/metrics.csv).