## Slide 1
Same-Frame Pixel-Level A/B Display: turning the picture itself into an instrument
A Zynq-7020 SoC takes 512×300 video over GbE, an SD card or its own generated pattern, runs geometry and a nine-stage effect chain entirely in the PL, and drives 1024×600 HDMI where everything left of an adjustable seam is the unprocessed frame and everything right is the processed one - same read address, same clock cycle, same column.
One scanline, two taps. Seam position is a control bit, not a second stream.
Board build r97 - bit md5 ef03eea4886e
PIPELINE RGMII -> self-written UDP/IP/MAC receive chain -> DDR frame buffers (ping-pong) -> geometry (zoom 0.25-2.00x; rotation with angle-driven auto-fit so the rotated frame always stays on panel; bilinear interpolation on both the zoom and the rotation path) -> 9-stage effect chain (15-cycle fixed) -> A/B seam mixer -> OSD -> HDMI/TMDS, with a bare-metal PS control plane (a few hundred lines) and a hardware link-health engine read out three ways: on screen, over JTAG, over serial.
What is new - four claims, each falsifiable
1 The display is the measurement. Per-pixel A-B on one scanline; the seam can be fixed, swept, or pinned in image domain so it follows zoom and rotation instead of sliding across the picture.
2 Health is counted in hardware, not asserted in a report. Received / dropped / corrupt / CRC / frame-gap statistics with three independent read-outs, and a source arbiter whose state is machine-readable - SRC:ETH|SD|TEST on screen is the actually selected source.
3 Bad frames do not reach the panel. Triple commit gate (row bitmap and byte budget and no-corrupt-flag) plus a blanking-window-atomic copy with a watchdog: a torn update is discarded and the previous frame is kept.
4 Reproducibility is engineered, not claimed. One command runs the 20-item gate suite (timing, resources, port widths, CDC pairs, document encoding / currency / line-citations) plus full-frame testbenches pinned by md5 to the RTL they checked; every criterion must be able to turn red, and every fix has a mutation control.
Key metrics - from data/metrics.csv
Pixel clock / panel 50 MHz, 1024x600 @ 59.5 Hz
End-to-end latency 33.34 ms mean (min/avg/max 20 / 33.34 / 51), PC to screen at 30 fps
Frame-interval jitter 33.33 ms mean (22 / 33.33 / 45)
Ingress, zero loss 0 dropped, 0 corrupt in 9000 frames over 300 s at 15 MB/s (RGB565)
Overload, not yet lossy 116.7 fps (about 36 MB/s, 287 Mbps) with no lost word - no maximum fps is claimed
SD playback rate 29.8 - 30.0 fps from a pre-converted frame sequence
Timing (post-route) setup WNS +0.720 ns, hold WHS +0.033 ns, 0 of 50890 endpoints failing
Resources LUT 14379 (27.03 %), FF 8079 (7.59 %), BRAM 95/140 (67.86 %), DSP 19/220
Power / temperature 2.207 W dynamic and 52.5 C estimated junction (tool confidence Low); on-die XADC reads 63.1 - 63.4 C on the board
HONEST BOUNDARIES Absolute WNS / WHS deltas are neither gain nor loss here - equivalent sources measured a 0.4 ns placement swing between builds. One per-pixel criterion is left deliberately red, documenting an unfixed frame-head wrap-around. Only xsim is available, so simulation-only divergences are closed out with on-board evidence. End-to-end figures are one round's measurement, not a fleet.
Tool chain: Vivado / Vitis 2025.2.1 - device xc7z020clg484-2 - sources on GitHub (MIT). Every number above names the report it came from (timing_summary.rpt, utilization.rpt, power.rpt, data/metrics.csv), reconciled row by row by src/host/metric_recheck.mjs: 9 rows judged, 0 red.